| Engine |  |
| --- | --- |
| Type | V8, 90° – Direct Injection – Dry Sump |
| Bore and stroke | 94 x 81 mm (3.7 x 3.2 in) |
| Overall displacement | 4497 cm3 (274.4 cu in) |
| Compression ratio | 14.0:1 |
| Maximum power** | 445 kW (605 cv) at 9000 rpm |
| Specific power output | 135 cv/l (1.62 kW/cu in) |
| Maximum torque | 540 Nm (398 lb ft) at 6000 rpm |
| Maximum revs (limiter) | 9000 giri/min |
| Dimensions and weight |  |
| Length | 4571 mm (180.0 in) |
| Width | 1951 mm (76.8 in) |
| Height | 1203 mm (47.4 in) |
| Wheelbase | 2650 mm (104.3 in) |
| Front track | 1679 mm (66.1 in) |
| Rear track | 1632 mm (64.3 in) |
| Dry weight* | 1290 kgf (2844 lbf) |
| Kerb weight* | 1395 kgf (3075 lbf) |
| Weight distribution | 42% front, 58% rear |
| Weight/power ratio | 2.13 kg/cv (6,39 lbf//kW |
| Fuel tank capacity | 86 l (22.7 US gallon) |
| Tyres and wheels |  |
| Front | 245/35 ZR20 J9” |
| Rear | 305/30 ZR20 J11” |
| Carbon-ceramic braking system |  |
| Front | 398x223x36 mm (15.7 x 8.8 x 1.4 in) |
| Rear | 360x233x32 mm (14.2 x 9.2 x 1.3 in) |
| Electronic control systems |  |
| ESC | Stability control |
| High performance ABS/EBD | High performance anti-lock braking system/electronic brake force distribution |
| F1-Trac | F1 traction control |
| E-Diff 3 | Third generation electronic differential |
| SSC | Side slip angle control |
| Frs SCM-E | Magnetorheological suspension control with frequency analysis system and twin solenoids |
| Gearbox |  |
| 7-speed F1 dual-clutch transmission |  |
| Performance |  |
| Maximum speed | > 325 km/h (>202 mph) |
| 0-100 km/h (0-62 mph) | 3,0 sec |
| 0-200 km/h (0-124 mph) | 9,1 sec |
| 0-400m (0-437 yd) | 10,7 sec |
| 0-1000m (0-1093 yd) | 19,4 sec |
| 100 – 0 km/h (62 – 0 mph) | 31 m (101.7 ft) |
| Fiorano lap time | 1’23’’5 |
| Fuel consumption and emissions (ECE + EUDC combined cycle) |
| Fuel consumption*** | 11,8 l/100 km |
| CO2 emissions*** | 275 gr/km |
| *With optional equipment |  |
| **Including 3.7 kW by ram effect |  |
| *** Combined cycle with HELE system (ECE+EUDC) |  |